## Slide 1
The data link layer is responsible for moving frames from one hop (node) to the next.
It is also responsible for error control, framing, flow control, addressing, media access control.
DATA LINK LAYER

## Slide 2: Error Detection and Correction
Data can be corrupted during transmission. Some applications require that errors be detected and corrected.
Types of Errors

## Slide 3
Single-bit error
In a single-bit error, only 1 bit in the data unit has changed.

## Slide 4
Burst error
A burst error means that 2 or more bits in the data unit have changed.

## Slide 5
Parity Checking
Single Bit Parity:
Detect single bit errors

## Slide 6
Example of Single Parity Code
Dataword (7 bits): (0, 1, 0, 1, 1, 0, 0)
Check Bit: b8 = (0 + 1 +0 + 1 +1 + 0) mod 2 = 1
Codeword (8 bits): (0, 1, 0, 1, 1, 0, 0, 1)
If single error in bit 3 : (0, 1, 1, 1, 1, 0, 0, 1)
  # of 1’s =5, odd
  Error detected
If errors in bits 3 and 5: (0, 1, 1, 1, 0, 0, 0, 1)
  # of 1’s =4, even
  Error not detected

## Slide 7
Process of error detection in block coding

## Slide 8
Cyclic redundancy checking (CRC) codes provide error detection for large blocks of data.
A group of error control bits is appended to the end of the block of transmitted data.
Cyclic redundancy checking

## Slide 9
Division in CRC encoder
Subtraction: logical XOR operation

## Slide 10
Division in the CRC decoder for two cases

## Slide 11
Polynomial to represent a binary word

## Slide 12
CRC division using polynomials

## Slide 13
Standard polynomials

## Slide 14
Given the message 100100 and the divisor 1101, Find the CRC.
Question
Solution